## Slide 1: Molten Salt Reactors
Louisiana Nuclear Society
Rowland Linford
March 19, 2019
Back to the future

## Slide 2
What is a molten salt reactor?
A molten salt reactor (MSR) is a type of nuclear reactor that uses liquid fuel instead of the solid fuel rods used in conventional nuclear reactors.
Why Are They Such a Hot Topic?
High temperature operation for hydrogen generation and other process heat.
Low pressure operation making radiation containment easier during transient conditions.
Generate less high level waste.
No fuel manufacturing.
Potential to “burn” fuel wastes and use alternate fuels easily.
Better stability and safety

## Slide 3: History
Aircraft Applications first major scale experiment
  Aircraft Reactor Experiment late 1940’s
    Extremely long range bombers in the air at all times
    Very high power density and power levels needed for thrust
    ARE reactor operated for 100 hours (1954)
      Na-Zr-U molten fuel pumped though Be blocks
      Sodium secondary fluid
      Inconel piping and structural material
      Achieved temperatures of 8600 C and 100 MWh energy
    Operating reactor (89 flights) flown in a Convair B-36 aircraft (not as an engine)
    Key issues were weight and crew shielding
  Other reactor tests run in INEL produced successful engines
  ICBM capability and development killed the aircraft nuclear programs

## Slide 4
Operated at Oak Ridge 1965 to December 1969
  Follow-on effort from ANP to develop commercial MSR power plants
  Alvin Weinberg key leader in the effort at ORNL
Design
  10-MW power - thermal spectrum core (actually 8MW due to design error)
    Single carrier fluid design
    Mixture of enriched LiF-BeF2-ZrF4(“ﬂibe”)
    Combined with ThF4 and/or UF4 fuel
    Unclad pyrolytic graphite moderator Structural and piping was Hastelloy-N (nickel alloy)
    Secondary coolant was molten LiF-BeF2
    No online fuel processing
Molten Salt Reactor Experiment

## Slide 5
MSRE Schematic

## Slide 6
MSRE Operating Experience
MSRE was a successful experiment
  Operation was reliable
  Radioactive liquids and gases were contained
  Corrosion could be limited effectively with Hestalloy
  UF salts were stable and compatible with other materials
  Single-fluid system worked
  Operation was acceptable with 233U, 235U or 239Pu
  U could be removed completely by fluoridation
  Did not include online reprocessing
What happened next
Modest effort until 1980
1000 MWe MS Breeder was designed
LiF-BeF2 – ThF4 - UF4 fuel salt
Secondary coolant NaF-NaBF4
Effort stopped to focus on LMFBR
ANP Engine at EBR-1 Site

## Slide 7: Current Day Overview
Decisions, decisions, decisions
  What applications and options are important
  Who is involved
  What is the cost? How is it financed/developed?
  What are limiting issues for full-scale application?
  What is a comprehensive safety analysis?
  What are the problems for site rehabilitation after end-of-life.
  Non-proliferation issues.
What fuel, Th or U?
  May be an issue independent of MSR
One of several concepts: Brayton cycle 40-44% efficiency

## Slide 8: Brayton Cycle Operation
High Temperature yields better efficiency and more applications

## Slide 9: MSR Advantages
Walk-away safe
  The core is already melted
  Negative temperature and void coefficients
  Lower fissile and radioactive inventory
  Low pressure operation - near atmospheric
  Freeze plugs melt at high temperatures dumping the core to subcritical “tanks”
  No operator action needed for fuel dumping
High temperature operation
  Broadens process applications such as hydrogen generation
  Raises efficiency to 40-44% range compared to LWRs at ~32-34%
Can be used to “burn” existing spent fuel (about 96% of the waste for LWRs)
Smaller amount of waste material
More efficient nuclear fuel usage
  No solid fuel assembly
  Online refueling
Waste not useful for future weapons applications
Fuel conversion and breeding easier with continuous reprocessing

## Slide 10
Radiotoxic Waste Perspective
Thorium Conversion Single Salt Concept
Important Features of MSRs

## Slide 11: Development Issues and Design Questions
Molten salt reactor (MSR) verses high temperature reactor (FHR)
FHR
  Has a solid core structure with fluorine salt coolants
  Achieves higher temperatures than the MSR
  Higher power densities than gas cooled high temperature designs
  Requires fuel fabrication
  Retains the passive safety features
  What fuel design: TRISO pebbles or rodded fuel
MSR
  Operates in broad range of neutron energy spectrum (burns, converts and breeds)
  Minimized wastes from fission but serious irradiation of components by circulated fuel
  Burns actinides in spent fuel as a recycled fuel function
  No fuel assembly required
  Two salt system verses single salt system for conversion or breeding advantages

## Slide 12: Development Issues and Design Questions
Salt types
  Lithium salts require enriched Li-7 to eliminate tritium generation
  Good news natural lithium is 92.4% Li-7
  Bad news – it still needs to be enriched to 99.99%
  Worse news – US would need to scale up production or purchase abroad (Russia or China?)
  Fluoride salts
    Good heat transfer, better energy retention than water, low vapor pressure at temperature, inert to key metals
    Require close monitoring to remain in a reduced state and avoid corrosion
    Have small neutron cross sections
    Melts at about 4590C and boils at about 14300C
    LiF-NaF-KF melts at 4540C and boils at 15700C but absorbs more neutrons
    Cl may be a good replacement for F but requires almost pure Cl37
Beryllium
  Toxicity is not desirable
  Avoiding it would require higher temperatures
Full scale system may turn up other corrosion issues

## Slide 13: Development Issues and Design Questions
Mobile fission products plating out – inventory accountability issues
Remote maintenance required due to high temperatures and high radiation
How to control tritium production elimination
Some fairly complex chemistry to remove actinides (cleanup of bred fuel for reuse)
Online fuel processing development
Thorium or Uranium Cycle development

## Slide 14
Thorium | tonnes
Brazil | 632,000
Australia | 595,000
USA | 595,000
Egypt | 380,000
Turkey | 374,000
Venezuela | 300,000
Canada | 172,000
Russia | 155,000
South Africa | 148,000
China | 100,000
Norway | 87,000
Greenland | 86,000
Finland | 60,000
Sweden | 50,000
Kazakhstan | 50,000
Other countries | 1,725,000
World total | 6,355,000
Uranium | tonnes | %
Kazakhstan | 842,200 | 14%
Canada | 514,400 | 8%
Russia | 485,600 | 8%
Namibia | 442,100* | 7%
South Africa | 322,400 | 5%
China | 290,400 | 5%
Niger | 280,000* | 5%
Brazil | 276,800 | 5%
Uzbekistan | 139,200* | 2%
Ukraine | 114,100 | 2%
Mongolia | 113,500 | 2%
Botswana | 73,500* | 1%
Tanzania | 58,200* | 1%
USA | 47,200 | 1%
Jordan | 43,500 | 1%
Other | 280,600 | 4%
World total | 6,142,600 | 
World Supplies of Uranium and Thorium

## Slide 15: Breeding New Thorium Fuel
Non-proliferation issue of breeding new fuel (also an issue with Uranium-Plutonium cycle)
  Thorium fuel application requires breeding or conversion since 233U does not exist in nature
  233U is produced from 232th by a neutron absorption becoming 233Pa that decays to 233U
  ( 232th 233Pa+β 233U)
  Pa removal highly desirable due to high absorption cross section
  233Pa decays with a 27 day half-life before becoming 233U
  Pure 233U is a ready-made nuclear weapons grade material
  Inventory tracking of fissile isotopes is difficult due to the core circulation and plate-out of of the fuel actinides
NOT A PROBLEM FOR OPERATIONAL TRANSIENTS OR FOR BURNING OR CONVERSION WHERE THE 233U STAYS IN THE FUEL!

## Slide 16: Who is playing and What Designs
China SINAP and US cooperation on solid fuel designs
China MSR design
Russia actinide recycler and transmuter (MOSART/MARS)
European community/Netherland SAMOFAR
US AHTR and FHR and LFTR, Thorcon, Southern Co MCFR, GE Hitachi
UK MOLTEX SSR
Canada Terrestrial Energy
Transatomic Power TAP
Japan Fuji
Denmark Seaborg SWaB
Elysium Industries US/Canadian
India MSBR

## Slide 17: Chinese Program (SINOP)
Technology R&D
  Includes fuel fab, online salt reprocessing, technology of pyro processing
  Corrosion and material lifetime evaluation for development reactors
  Reactor design development for experimental and demo systems
  Develop design, safety analysis and technical standards
  Develop high temperature applications and hydrogen production
  Very complete R&D to develop the design, design processes and manufacturing of MSRs
About 400 staff level
Developing two test reactors TMSR-Sf1 and TMSR-LF1 for solid fuel and liquid fuels

## Slide 18
Power 10MWt
Lifetime 20year
Operation time 100 EFPD for single batch of fuel
Average power density 4.0 MW/m3
Fuel element / abundant / 235U load 6cm ball / 17.0% /15.6 kg Coolant（1stloop，2ndloop）FLiBe（99.99%Li7 ，FLiNaK Structure material N alloy, graphite
Reactor coolant inlet temperature 6000C
Reactor coolant outlet temperature 6500C
Vessel temperature / pressure design 7000C / 0.5MPa (abs.) Vessel upper cover temperature designed <3500C
1st/2ndloop coolant flow rate 84 kg/s / 150kg/s
Cover gas/ pressure Ar/ 0.15MPa(abs.)
SF1 Design Parameters

## Slide 21
Safety Assessment of the Molten Salt Fast Reactor (SAMOPAR)
Prove safety concepts of Thorium in the breeding mode
Advanced experimental and numerical methods
Break though in safety and optimal waste management
Only one in which the Pa-233 can be stored in a hold-up tank to let it decay to U-233.
11 participants and is mainly undertaken by universities and research laboratories
European Community Program

## Slide 22
US Design and Development: FHR
FHR a high-temperature reactor that can conceptually have an outlet temperature of 1000 °C
Core design can be graphite prismatic blocks or graphite pebble form but is designed to be a burner
Operates with liquid salt coolant
Pebble form of the fuel is called TRISO
Spherical fuel pebble with several regions
Center is uranium oxide, carbide or UCO covered by layers of carbon materials
There are four layers of carbon, a dense layer of pyrolytic carbon and finally silicon carbide surrounding the uranium fuel
Advantages
  High temperature
  Low Pressure operation
  High power density
  High thermal efficiency
  Passive safety systems
  Better retention of fission products if an accident occurs
TRISO Fuel Pebble
FHR Reactor

## Slide 23: Liquid Fluoride Thorium Reactor and FLiBe LFTR
Both designs are two-fluid MSRs
One fluid is the fuel and the other is the fertile fluid
Rapid power changes possible so they can load follow
Inexpensive to build and operate
LFTR
  Breeding is done in a blanket with FLiBe and ThF as fertile material
Pa-233 captured and allowed to decay to U-233
U-233 converted to fuel and returned to the reactor
FLiBe LFTR
Uses FLiBe as the salt for both fuel and breeding
Breeding salt includes Th
Fuel salt circulates through graphite “logs”
Secondary loop coolant is BeF2-NaF

## Slide 24: ThorCon
Underground siting
Scale up of the MSRE reactor
Block assembly in a factory and shipped to site
Four year change-out cycle of key components
Walk-away safety by draining fuel during an accident
Closed steam cycle for higher efficiency
The ThorCon Nuclear Island. This entire structure is underground

## Slide 25: Terrestrial Energy IMSR
Graphite-moderated thermal reactor
Fuel enrichment lower than 5%
Core and moderator replaced as a unit every 7 years
U235 fuel (UF4) in a fluoride carrier salt
Secondary fluid is ZrF4-KF
Completed the first of three phases in the Canadian Nuclear Safety Commission's pre-licensing vendor design review
Three size units 80 MWt, 300 MWt and 800 MWt
Aim is first operation by 2030

## Slide 26: First Business Casualty
Transatomic Power announced it is shutting down operations 9/25/2018
Did not believe they can catch up to the leaders
Will provide all design information as open source

## Slide 27: Summary
We are at the “gold rush” stage
Early stage development
  Effort is more software and concepts
  Less expensive stage of evolution
  Overly optimistic aura in the excitement of great new things
  There will be an inevitable “shake-out” of ideas, providers and demonstrations
Now is the time for clear thinking and serious process development
Big issues looming
  Regulatory process
  Design process
  Operations process
  Thorium potential
  Breeding and non-proliferation resolution
Expect development money and support will be a big factor

## Slide 28
Hang on: this next generation will be very interesting