## Slide 1: NuScale SMR
An Innovative Design by a Nuclear Newcomer
Rowland Linford
Dylan Robideaux

## Slide 2: Background
Small Modular Reactor (SMR) interest
  Lower manufacturing costs
  Safety upgrading
  Easier licensing process
  Flexible generation capabilities – off grid possibilities
  Less risk for operation
What is the development scene
  World Nuclear Association (March 2018 update)
  Some 86 designs listed
    32 were LWR – mostly PWR based designs
    2 PHWR
    16 gas cooled - mostly helium
    6 sodium cooled
    9 molten core
    Various other designs (traveling/standing wave, lead, bismuth cooled, etc)
  International interest very high
Several non-traditional players

## Slide 3: DOE Participation
Provided partial DOE funding for two systems
  B&W mPower
    Integral PWR design
    500 MWt, 180 Mwe
    Struggling with funding support to finish initial implementation
  NuScale
    Integral PWR design
    160 MWt, 50 Mwe
  Use of PWR technology simplifies both design and licensing

## Slide 4: NuScale Reactor
What is the NuScale Reactor?
  NSSS is Factory Manufactured
    NSSS factory prefabricated
    Shipped by rail, truck or barge
  Natural Circulation Cooling:
    Inherently safe – eliminates major accident scenarios
    Improves economics – eliminates pumps, pipes and valves
  Large Natural Heat Sink simplifies and enhances safety
  Proven Technology
  Below Ground Siting
    Enhances security and safety

## Slide 5: NuScale Reactor
NuScale Power ModuleTM details:
Thermal capacity – 160 MWt
Electrical capacity – 50 MWe (gross)
Capacity factor – >95 percent
Dimensions – 76' x 15' cylindrical containment vessel module containing reactor and steam generator
Weight – ~ 700 tons as shipped from fabrication shop
Transportation – Barge, truck or train
Cost – Numerous advantages due to simplicity, off-the-shelf standard items, modular design, shorter construction times, <$5,100/KW
Fuel – Standard LWR fuel in 17 x 17 configuration, each assembly 2 meters (~ 6 ft.) in length; 24-month refueling cycle with fuel enriched less than 4.95 percent
Natural Circulation

## Slide 6
Single Power Module Reactor and TG Units Coupled

## Slide 7
Convection – energy from the nuclear reaction heats the primary reactor coolant causing it to rise by convection and natural buoyancy through the riser, much like a chimney effect
Conduction – heat is transferred through the walls of the tubes in the steam generator, heating the water (secondary coolant) inside them to turn it to steam. Primary water cools.
Gravity-colder (denser) primary coolant “falls” to bottom of reactor vessel, cycle continues

## Slide 8
Helical Steam Generator

## Slide 9: Natural Circulation Inside RPV
  Steam Generator is fully integrated within the reactor pressure vessel (RPV)
  Contained in annulus between the upper riser and the RPV shell
  Feed flow enters the feed plenums, flows upward through the inside of the tubes and is discharged via the steam headers
  Reactor coolant flows upward through the upper riser, is turned by the pressurizer baffle plate, and flows down through the helical bundle

## Slide 10: Off-the-Shelf Items
  Reactor Vessel and Containment Materials - Used in Commercial Nuclear Plant Operations
  Magnetic Jack Control Rod Drive Mechanisms
  Control Rods and Fuel Assemblies
  Skid Mounted Steam Turbine
  Air-cooled Generators
  Condenser
  Feedwater system
  Emergency Core Cooling System Valves
  Fuel Handling Cranes and Fuel Mast

## Slide 11
Ease for transportation from factory

## Slide 13: Overall Plant Performance

## Slide 15
reactor building crane
reactor pool
weir
reactor vessel
flange tool
containment vessel flange tool
NuScale Power Module
biological shield
spent fuel pool
Reactor Building Side View
refueling machine

## Slide 16: NuScale Safety Advantages
  Natural Convection for Cooling
    Inherently safe, gravity-driven natural circulation of water over the fuel
    No pumps, no need for emergency generators
  Seismically Robust
    Containment is submerged in a pool of water below ground in an robust building
    Reactor pool attenuates ground motion and dissipates energy
  Simple and Small
    Reactor is 1/20th the size of large reactors
    Integrated reactor design, no large-break loss-of-coolant accidents
  Defense-in-Depth
    Multiple additional barriers to protect against the release of radiation to the environment
    High-strength stainless steel containment 10 times pressure capability than typical PWR
  Water volume to thermal power ratio is 4 times larger resulting in better cooling
  Reactor core has only 5% of the fuel of a large reactor
  50 MWe Reactor Module

## Slide 17: NuScale Nuclear Safety Considerations
Safety starts with underground installation of the NSSS

## Slide 18
NuScale Power Module
Combined Containment Vessel and Integral Reactor System
Typical Pressurized-Water Reactor
Containment & Reactor System

## Slide 19: NuScale Safety Time Scale
WATER COOLING
BOILING
AIR COOLING
Triple Crown of Safety

## Slide 20: Decay Heat Removal 0 to 3 Days Post Accident

## Slide 21: ECCS Mode 3 to 30 Days Post-Accident

## Slide 22: Core Damage Probability

## Slide 24: NRC agrees NuScale SMR needs no back-up power
The US nuclear regulator is satisfied that NuScale Power's small modular reactor (SMR) design can operate safely without the need for safety-related electrical systems. The reactor uses passive safety features, such as relying on convection, not pumps, to circulate water in the primary circuit.

## Slide 26
Twelve-reactor simulated control room commissioned in May 2012 for Human Factors Engineering development

## Slide 27: A Brief History of NuScale SMR
  From 2000 to 2003 NuScale participated in a DOE funded program for development of passive safety systems
  After 2003 Oregon State University Built a one-third scale natural circulation heated version of their plant
  OSU granted exclusive rights to NuScale for nuclear plant design and use of the test facility
  2008 NuScale notified the NRC it would pursue Design Certification for it’s technology
  2011 Fluor Corporation became the primary investor and to facilitate commercialization
  2013 NuScale announced WIN, a western state collaboration to implement NuScale SMRs
  Rolls Royce joined Fluor to add design and manufacturing capabilities
  DOE added $217M matching funds to support the further development of the design and to secure a Design Certification from the U.S. Nuclear Regulatory Commission
  2014 NuScale Power LLC and Enercon Services Inc. (ENERCON) announced a new strategic partnership

## Slide 28: A Brief History of NuScale SMR
  2015 Successfully installed a full-length helical coil steam generator (HCSG) at the SIET S.p.A.(Italy)
  Fabrication and assembly of a full-scale, upper module mockup of the NuScale Power
  Module was completed
  NuScale Power and Ultra Electronics announced a new strategic partnership
  Contracted for AREVA to manufacture first core and reload fuel assemblies for NuScale’s small modular reactor
  2016 Completion of a study commissioned from the UK National Nuclear Laboratory
  Asked NRC to approve NuScale DCA
  2017 Submitted completed DCA to NRC

## Slide 29: NuScale Reactor
Design Certification Application (DCA) (NuScale)
  Tendered December 2016
  Completed January 2017
  NRC Staff now reviewing the DCA (NRC)
  NuScale believes the review is somewhat ahead of schedule
  Preliminary Safety Evaluation Report (SER) and requests for additional information – 4/16/18 (NRC schedule)
  Final SER no open items – 9/8/20 (NRC schedule)
  First COL application expected 2019 (UAMPS or other applicant)
  Expected operation 2026 (NuScale schedule)
  Note: Schedule disconnect between NuScale and NRC

## Slide 30: Major Participants
SMR Builder- NuScale
Customer - Utah Associated Municipal Power Systems (UAMPS)
Regulatory review - NRC
Site provider and partial funding - DOE
Location - Idaho Nuclear Engineering Laboratory (INEL)
Oregon State University (Corvallis)
Expect no need to develop a prototype due to PWR type technology
Fluor Corporation – funding and fabrication
Rolls Royce - Commercialization support and UK connection

## Slide 31: NuScale Innovations and Advantages
Underground NSSS Installation
Natural Circulation PWR Cooling System
Passive Safety System based on Natural Circulation
Modular Plant Concept
Factory Fabrication of NSSS
Helical Internal Steam Generator inside RPV
Based on existing PWR technologies

## Slide 32
Backup Slides